## Slide 1: CGNs in IP What are you going to do about it?
Mark Kosters, ARIN
Geoff Huston, APNIC

## Slide 2
The mainstream telecommunications industry has a rich history

## Slide 3
The mainstream telecommunications industry has a rich history
…of making very poor
technology choices

## Slide 4
The mainstream telecommunications industry has a rich history
…of making very poor
technology guesses
and regularly being
taken by
surprise!

## Slide 5
So, how are we going with the IPv4 to IPv6 transition?

## Slide 6: The Amazing Success of the Internet
2.3 billion users!
4 online hours per day per user!
4% of the world GDP

## Slide 7: The Amazing Success of the Internet
2.3 billion users!
4 online hours per day per user!
4% of the world GDP
Time
Just about anything about the Internet

## Slide 8: Success-Disaster

## Slide 9: Success-Disaster
Fractions
of a percent!

## Slide 10: The Original IPv6 Plan c. 1995
IPv6 Deployment
Time
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet

## Slide 11: The Revised IPv6 Plan c. 2005
IPv6 Deployment
2004
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet
2006
2008
2010
2012
Date

## Slide 12: Oops!
We were meant to have completed the transition to IPv6 BEFORE we completely exhausted the supply channels of IPv4 addresses!

## Slide 13: Today’s Plan
IPv6 Deployment
IPv4 Pool
Size
Size of the
Internet
IPv6 Transition
Today
Time
?
0.8%

## Slide 14: Transition ...
The downside of an end-to-end architecture:

## Slide 15: Transition ...
The downside of an end-to-end architecture:
  There is no backwards compatibility across protocol families
  A V6-only host cannot communicate with a V4-only host

## Slide 16: Transition ...
We have been forced to undertake a “Dual Stack” transition:

## Slide 17: Transition ...
We have been forced to undertake a “Dual Stack” transition:
  Provision the entire network with both IPv4 AND IPv6

## Slide 18: Transition ...
We have been forced to undertake a “Dual Stack” transition:
  Provision the entire network with both IPv4 AND IPv6
  In Dual Stack hosts configure the hosts’ applications to prefer IPv6 to Ipv4

## Slide 19: Transition ...
We have been forced to undertake a “Dual Stack” transition:
  Provision the entire network with both IPv4 AND IPv6
  In Dual Stack hosts configure the hosts’ applications to prefer IPv6 to Ipv4
  When the traffic volumes of IPv4 dwindle to insignificant levels, then its possible to shut down support for IPv4

## Slide 20: Dual Stack Transition ...

## Slide 21: Dual Stack Transition ...
We did not appreciate the operational problems with this dual stack plan while it was just a paper exercise

## Slide 22: Dual Stack Transition ...
We did not appreciate the operational problems with this dual stack plan while it was just a paper exercise
The combination of an end host preference for IPv6 and a disconnected set of IPv6 “islands” created operational problems
  Protocol “failover” from IPv6 to IPv4 takes between 19 and 108 seconds (depending on the operating system configuration)
  This is unacceptably slow
Attempting to “bridge” the islands with IPv6-in-IPv4 tunnels created a new collection of IPv6 path MTU Discovery operational problems
  There are too many deployed network paths contain firewall filters that block all forms of IMCP, including ICMP6 Packet Too Big
Attempts to use end-host IPv6 tunneling also presents operational problems
  Widespread use of protocol 41 (IP-in-IP) firewall filters
  Path MTU problems

## Slide 23: Dual Stack Transition
Signal to the ISPs:
  Deploy IPv6 and expose your users to operational problems in IPv6 connectivity
  Or
  Delay IPv6 deployment and wait for these operational issues to be solved by someone else
So we wait...

## Slide 24: And while we wait...
The Internet continues its growth
And without an abundant supply of IPv4 addresses to support this level of growth then the industry is increasingly reliant on NATs:
  Edge NATs are now the defacto choice for residential broadband services at the CPE
  ISP NATs are now the defacto choice for 3G and 4G mobile IP services

## Slide 25: NATTing the Net
In 2012:
  The RIRs made 8,547 allocations to LIRs, allocating a total of 114M IPv4 addresses
  The routing table grew by 120M addresses
  The ISC host survey* indicates a growth of ~60M visible hosts
  BUT
    In 2012 Apple sold ~110M iPhones and ~60M iPads and they have ~30% market share globally
    This implies that some ~560M mobile devices were sold in the last 12 months
  It appears that the NATTed Internet grew by ~550M devices in the last 12 months!
* http://www.isc.org/solutions/survey

## Slide 26: The Anatomy of NATs
NAT
“Interior”
“Exterior”
Public Address Space
Private Address Space
Translation Table
Source address (private)
Destination address
Source port (private)
Destination port
Source address (public)
Destination address
Source port (public)
Destination port
Source address (private)
Destination address
Source port (private)
Destination port
Source address (public)
Destination address
Source port (public)
Destination port

## Slide 27: The Anatomy of NATs
Translation Table:
Interior Exterior
Binding Time Protocol Address/Port /Address/Port
TCP or UDP
Timer
Interior IP address
and Port number
Exterior IP address
and Port number

## Slide 28: Design Parameters
TCP
Open NAT Binding:
  Interior SYN
Access NAT Binding
  Symmetric (same exterior IP address, same exterior port)
Release NAT Binding:
  Interior RST
  Interior FIN?
  Exterior FIN?
  Exterior RST?
  Timer?
UDP
Open NAT Binding
  Interior packet
Access NAT Binding
  Symmetric (same exterior IP address, same exterior port)
  Full cone (any exterior IP address, any exterior port)?
  Restricted cone (same exterior IP address, any exterior port)?
  Port-restricted code (any exterior IP address, same exterior port)?
Release NAT Binding:
  Timer?
Port Control Protocols
STUN/TURN
PCP relay of UPnP and NAT-PMP

## Slide 29: Design Parameters
TCP
Open NAT Binding:
  Interior SYN
Access NAT Binding
  Symmetric (same exterior IP address, same exterior port)
Release NAT Binding:
  Interior RST
  Interior FIN?
  Exterior FIN?
  Exterior RST?
  Timer?
UDP
Open NAT Binding
  Interior packet
Access NAT Binding
  Symmetric (same exterior IP address, same exterior port)
  Full cone (any exterior IP address, any exterior port)?
  Restricted cone (same exterior IP address, any exterior port)?
  Port-restricted code (any exterior IP address, same exterior port)?
Release NAT Binding:
  Timer?
Port Control Protocols
STUN/TURN
PCP relay of UPnP and NAT-PMP
Different NATs make different choices in these design parameters
Applications then have to “discover” the particular behavioral type in order to perform non-trivial operations
This adds delay, complexity and fragility to the service model of the network

## Slide 30
Relieved pressure for IPv4 space
Is nearly everywhere
2 Party NATs
AKA Subscriber-Based NATs
Home Network
Middle Box
Internet
IPv4
192.168.0.0/24
IPv4
Globally Unique Address

## Slide 31
Adds a new non-unique realm in the Carrier
Adds more complexity but “slows” runout
3 Party NATs
AKA Carrier Grade NAT
Home Network
Edge NAT
Internet
IPv4 Private Space
192.168.0.0/24
IPv4
Globally Unique Address
Carrier
CGN
IPv4 Private Space
10.0.0/8

## Slide 32: Some Multi-NAT Issues
What is the aggregate NAT binding behavior as seen by an application?
How can an application “discover” this aggregate binding behaviour?
Can an application determine how many NATs (and of what type) are in its data path?
Does the carrier need a new private address space that is distinct from RFC1918 address space?
How does home-to-home work in this model?
Does this model become more complex with 3 NATs in series?
Home Network
Edge NAT
Internet
Carrier
CGN

## Slide 33: How Good Are NATs?
3-party rendezvous:
A knows about B and C
A tells B to contact C
Teredo is a good example here:

## Slide 34: NAT Failure
How well do NATs perform in supporting an application performing a 3-party rendezvous?
  One way to measure this is to test a common 3-party rendezvous application across a large number of clients
  So we measured it
  And we were pretty surprised

## Slide 35: Teredo Failure Rate
ICMP Exchange fails to complete
ICMP completed, but SYN Exchange fails to complete

## Slide 36: It’s NAT Traversal Failure
Teredo failure is around 35% of all connection attempts
  Obviously, this is unacceptably high!
  This is unlikely to be local filtering effects given that Teredo presents to the local NAT as conventional IPv4 UDP packets
  More likely is the failure of the Teredo protocol to correctly identify the behaviour mode of the local NAT device
  The ICMP failure rate comes from the limited number of UDP NAT traversal models used by the Teredo handshake protocol vs the variance of UDP NAT traversal models used in networks
  The SYN failure rate is a result of the Teredo protocol making incorrect assumptions about the NAT’s behaviour

## Slide 37: Working with Failure
A 35% connection failure is unworkable is almost all circumstances
But one particular application can thrive in this environment – Bit Torrent:
  The massive redundancy of the data set across multiple sources reduces the sensitivity of individual session failures
All other protocols fail under such adverse conditions

## Slide 38: CGN Deployment
What’s the likely outcome of widespread CGN deployment on today’s Internet?
  It’s TCP, UDP or failure!
  It’s simple client-server 2-party rendezvous or failure!
  It’s network path symmetry, or failure!
Really simple transactions in a restricted application environment will still function, but not much else can be assumed to work

## Slide 39: What’s the New New Plan?
If NATs make the network complex and fragile,
And the IPv6 deployment program continued to proceed at a geological pace,
Then what are we going to do to make the Internet work for the next 5 years of growth?
  And don’t say “SDN”
  Or “OpenFlow”

## Slide 40: What’s the New New Plan?
How can we pull the Internet though a middleware dense environment for the next 5 years?
  What application models are robust in a CGN-dense world
  How do CGNs break?
  How variable are CGNs?
  What will applications need to cope with?

## Slide 41: What would help
Can we perform wide scale measurements of NAT robustness?
Is there improvements that can be learned from testing?
How?

## Slide 42: And what would not
Inaction