## Slide 1: Authoritative Nameserver Selection and Recursive Resolvers
Geoff Huston
APNIC Labs
ICANN 82, March 2025
Notes: The selection of which authoritative DNS server to use by a user's DNS resolver of choice greatly determines the user experience when accessing the Internet. In the past some studies have looked at the behaviour of a set of implementations describing how they perform authoritative server selection and how they re-evaluate their choices in time [1]. Other studies have leveraged the RIPE Atlas infrastructure to observe DNS resolution of a researcher-owned domain name from various points on the Internet [2] We extend and complement these studies by using APNIC's distributed ad system to recruit several million end-users throughout the global Internet to observer the resolution selection process as well as its time evolution through a several day period. References [1] Secure Nameserver Selection Algorithm for DNS Resolvers. https://datatracker.ietf.org/doc/draft-zhang-dnsop-ns-selection/ [2] Recursives in the Wild: Engineering Authoritative DNS Servers https://ant.isi.edu/~johnh/PAPERS/Mueller17b.pdf

## Slide 2: Nameserver Questions
When configuring nameservers for a domain, or evaluating the various service offerings from nameserver platform providers there are some common questions:
  How many nameservers is “right”
  Can you have too many nameservers? If so, what number is “too many”?
  Unicast vs Anycast? Can I mix them together?
  What’s a “good” unicast configuration?
  What’s a “good” anycast configuration?
  What TTL should I use?
All of these questions are fine, but they need a context. The context here is the behaviour of DNS recursive resolvers.

## Slide 3: Nameserver Questions
When presented with multiple authoritative nameservers / multiple IP addresses how do recursive resolvers behave?
Once we have a handle on the answer to this question, we can then look at the next one:…
How do we maximize performance and resilience in authoritative nameserver configurations?

## Slide 4: The RFC’s say:
RFC1034: “The sorting [of nameservers]… may involve statistics from past events, such as previous response times and batting averages.”
Batting averages????

## Slide 5: Our Measurement
Use a domain with four unicast authoritative nameservers
Direct client systems to resolve unique DNS names using these nameservers
Track queries to each nameserver from each visible recursive resolver

## Slide 6: Our Measurement
Use a domain with four dual-stack unicast authoritative nameservers
Frankfurt
Mumbai
Singapore
112ms
267ms
205ms
Atlanta
208ms
154ms
60ms

## Slide 7: What are we expecting to see?
We anticipate seeing a “strong” preference to query the authoritative server with the lowest response time, and a regular querying of all other authoritative servers to see if their response times have changed.

## Slide 8: Some Lab Tests: Bind 9
Observing Bind 9 against the four nameservers using 1 query per second (test resolver is located in au)
The resolver tests the other authoritative servers to ensure that its is “attached” to the fastest server.
This ‘other server’ test appears to be irregular, with a slight bias towards the second-closest server

## Slide 9: Some Lab Tests: Unbound
Observing Unbound against the four nameservers using 1 query per second (test resolver located in au)
Unbound is not so clearly attached to the closest server (ap) and also queries Mumbai and Atlanta consistently.
The non-selected resolver (Frankfurt) is queried irregularly

## Slide 10: Some Lab Tests: Google 8.8.8.8
Observing Google 8.8.8.8 against the four nameservers using 1 query per second (stub resolver located in au)
The Google resolver appears to query all instances regularly.
There appears to be a slight preference to use the Singapore (ap) server

## Slide 11: Some Lab Tests: Cloudflare 1.1.1.1
Observing Cloudflare’s 1.1.1.1 resolver against the four nameservers using 1 query per second (stub resolver located in au)
There is a visible preference to use the servers located in Singapore (ap) and Mumbai (in)

## Slide 12: There is no common recursive resolver behaviour
In this small sample set we are not seeing a common behaviour across recursive resolvers
To optimize resolution performance the recursive resolver would prefer to direct most of its queries to the authoritative server that responds in the shortest time
However, the resolver would also like to track all other servers to ensure that its preferred choice of server is still optimal
It is not clear what units of time are used compare servers’ response performance, as some resolvers appear to treat a subset of servers with diverse query/response times as equivalent

## Slide 13: Let’s scale up the measurements
We’ll use an ad-based measurement platform to enrol some 25M stub resolvers per day and observe the interaction between the various recursive resolvers used by these stub resolvers and their behaviour against these four unicast authoritative servers

## Slide 14: What we see – 1 Hour Profile
This is a resolver operated by Bharti Airtel in India:
It appears to spread its query load roughly equally across the servers in Mumbai, Frankfurt and Singapore
But none to Atlanta!

## Slide 15: What we see – 12 Hour Profile
This resolver passed 2 queries to the server located in Atlanta just 2 times in this 12 hour period
From this graph it is not evident if there is any preference between the other three nameservers – but maybe summary numbers can be more informative

## Slide 16: A one-week profile of this resolver
Server | Queries | Attachment Time (secs) | Longest attached Interval (secs)
Atlanta | 87 | 1 | 0
Singapore | 611,992 | 202,012 | 725
Frankfurt | 581,799 | 183,051 | 637
Mumbai | 300,751 | 32,153 | 580
How many seconds did the resolver “latch” onto this server?
What was the longest period spent asking ONLY this server
A large recursive resolver, located in India, appears to prefer distant servers that are located in Singapore and Frankfurt over a server
located in Mumbai

## Slide 17: 8 Day Profile of 100 Resolvers
The 100 recursive resolvers that processed the largest number of queries in an 8-day period (1 Dec – 8 Dec)
The size of the point indicates the relative amount of time the resolver appears to “latch” onto an individual server
Most queries
Fewer queries

## Slide 18: What proportion of Resolvers show “Attachment Preference”?
Use the most active 1,000 recursive resolvers
Define an “attachment preference” as maintaining an authoritative server selection for more than 60% of the time
  616 out of these 1,000 recursive resolvers show a strong attachment preference
Define “NO attachment preference” as having the major attachment for no more than 40% of the time
  53 out of the 1,000 recursive resolvers show a no attachment preference

## Slide 19: How “good” is this attachment preference?
Do recursive resolvers who have a strong attachment end up attaching to the server that is “nearest” to them?
Let’s combine ping RTT measurements with these resolver / server measurements

## Slide 20: For example:
2a01:e00:ffff:53:2::13 is a recursive resolver operated by free.fr in France
RTT Measurements for this resolver. The ping measurements for this resolver are:
Atlanta – 95.3ms
Singapore - 307.5ms
Frankfurt – 9.8ms
Mumbai – 241.6 ms
This resolver (located in Paris, France) was observed to query the Atlanta server 70% of the time, a resolver that was 85ms further “away” than the closest resolver (located in Frankfurt)

## Slide 21: Results
Of the 661 recursive resolvers that showed strong “attachment” for a single resolver (queried one server more than 60% of the time)
498 recursive resolvers responded to ping requests
Of these 498 resolvers:
  199 resolvers chose the server that had the lowest ping time
  The other 299 chose a more distant server
    The average additional RTT between the chosen server and the closest server for these 299 resolvers was 142.3ms

## Slide 22: Distribution of “Mismatch Times”
There is a strong signal of a time mismatch of <= 150ms
Is this indicative of some form of rounding of the resolvers’ internal recursive-to-authoritative delay timers of to a unit of 150 ms increments?

## Slide 23: What is this data telling us?
You can’t rely on the preference algorithm used by today’s recursive resolvers to make an optimal selection across a dispersed set of unicast servers that will select the fastest authoritative server
  i.e. even if you do a great job of deploying diverse unicast nameservers, recursive resolvers will likely muck it up and make sub-optimal selections of their “preferred” nameserver!

## Slide 24: How should you deploy a set of nameservers?
Assuming that you want to optimize both performance and availability…
A distributed collection of unicast nameservers is not going to give the best possible result
  Many recursive resolvers are not only poor at latching on to the fastest nameserver, but they latch onto a more distant nameserver, giving a worse resolution performance for non-cached name resolution
Perhaps a better approach is to use anycast nameservers
What do other domains do for their nameserver configuration?

## Slide 25: Let’s look the Root Zone
A small set of relatively intensely used domains whose performance and reliability is (supposedly) critical

## Slide 26: Profile of the Use of Nameservers
Root Zone:
  TLDs: 1,445
  Authoritative Nameservers: 5,998
  Average Nameservers per TLD: 4.2
  Distribution of Nameservers per TLD show strong preference for 4 or 6 nameserver names
  Dual Stack Nameservers: 5,687
  IPv4-only Nameservers: 321
  IPv6-only Nameservers: 3

## Slide 27: Unicast vs Anycast – Root TLD Nameservers
Unique IP addresses of nameservers: 9,014
Unicast IP addresses: 587
“Limited” Anycast addresses: 5,868 (rtt variance > 150ms)
“Diverse” Anycast IP addresses: 2,559 (rtt variance < 150ms)

## Slide 28: Unicast vs Anycast
TLDs served by only unicast nameservers: 8
TLDs served by a mix of unicast and anycast servers: 378
TLDs served by anycast servers only: 1,067
  TLDs served only by diverse anycast: 289
  TLDs served only by limited anycast: 202
  TLDs served by limited and diverse anycast: 576

## Slide 29: AS Diversity
In the root zone there are just 6 TLDs where all the zone’s nameservers are held in a single AS (and only 1 in a diverse anycast configuration)
On average each TLD has 10.1 distinct IP addresses of nameservers
On average each TLD has nameservers located in 3.4 origin Ases

## Slide 30: Tranco Top 1M Name set
20%
63%

## Slide 31: Nameserver Distribution
119,544 domains, or 12% of the total domain set, are each served by a (different) single IP address!
44,229 domains are served by just two IP addresses
13,498 domains are served by just three IP addresses.
At the other end of this distribution, there are two IP addresses that each serve 13,278 domains and a further four IP addresses that serve some 12,400 domains.

## Slide 32: Platform Concentration
Domains | AS | AS name, CC
364,918 | 13335 | CLOUDFLARENET, US
109,766 | 16509 | AMAZON-02, US
51,642 | 44273 | GODADDY-DNS, DE
23,539 | 397239 | SECURITYSERVICES, US
15,212 | 16276 | OVH, FR
14,155 | 15169 | GOOGLE, US
13,710 | 8075 | MICROSOFT, US
11,637 | 24940 | HETZNER-AS, DE
10,731 | 37963 | ALIBABA-CN-NET, CN
10,198 | 21342 | AKAMAI-ASN2, NL
9,775 | 16552 | TIGGEE, US
8,263 | 8560 | IONOS-AS, DE
7,881 | 62597 | NSONE, US

## Slide 33: Platform Type
Unicast-only platform | 205,204
Mixed Unicast and Anycast platforms | 80,442
Anycast-only platform | 562,364
Diverse Anycast | 369,254
Limited Anycast | 102,882
Mixed Diverse and Limited Anycast | 90,228
Outside of Cloudflare’s service portfolio few domains
Are served using a large-scale diverse anycast nameserver configuration
There is still a significant “legacy” group of domains served by unicast nameserver platforms

## Slide 34: Observations (1/3)
DNS recursive resolvers do not, on average, make an accurate selection of the “fastest” nameserver
  Which negates any potential performance benefits of a nameserver deployment approach of a geographically diverse collection of unicast nameservers
  Many recursive resolvers appear to use a timer with a granularity of around 150ms to select the “fastest” nameserver

## Slide 35: Observations (2/3)
Anycast nameserver deployments can produce better outcomes, but the effectiveness of this approach depends on the density of the anycast constellation
  Limited density anycast constellations may produce sub-optimal outcomes for some clients

## Slide 36: Observations (3/3)
Resilience can be provided through the use of multiple anycast service platforms
  How many such platforms is “optimal” is an open question
  More is not necessarily incrementally better, which leads to a suggestion of the use of 2 or 3 diverse anycast platforms, depending on the level of failover resilience you are after

## Slide 37: Questions?

## Slide 38: Overflow Slides

## Slide 39: Recent(ish) work
“Recursives in the Wild: Engineering Authoritative DNS Servers” Muller, Moura, Schmidt, Heidemann, 2017
https://ant.isi.edu/~johnh/PAPERS/Mueller17b.pdf
  “To meet their goals of minimizing latency and balancing load across NSes and anycast, operators need to know how recursive resolvers select an NS, and how that interacts with their NS deployments.”
  “… all name servers in a DNS service for a zone need to be consistently provisioned (with reasonable anycast) to provide consistent low latency to users.”

## Slide 40: Recent(ish) work
“Secure Nameserver Selection Algorithm for DNS Resolvers” Zhang, Liu, Song, Huque, October 2024
https://datatracker.ietf.org/doc/draft-zhang-dnsop-ns-selection/
  “Nameserver selection algorithms employed by DNS resolvers are not currently standardized in the DNS protocol”
  The document contains an informal description of the selection algorithms used in a number of commonly used recursive resolvers (Bind 9, Unbound, Knot, PowerDNS, Microsoft DNS)

## Slide 41: Unicast vs Anycast
How many of these IP addresses are carried in an anycast cloud?
  Query the IP address from a diverse set of locations(Atlanta, Frankfurt, Sao Paulo, Singapore, Australia)
  If the Name Server ID (NSID) is constant when queried from a diverse set of queries, then its reasonable to assume that the server’s IP address is not part of an anycast cloud (as we anticipate that different anycast instances will give a different NSID response)
  If the variance of DNS query times is not sufficiently large, then its reasonable to assume that the server’s IP address is part of an anycast service cloud.

## Slide 42: BUT - DNSSEC
The combination of multiple diverse nameserver providers, a DNSSEC-signed domain name, and online signing introduces some operational fragility, particularly when managing key rollover and algorithm rolls
This is still a not well charted space and operational incidents that impact TLD availability still occur